## Slide 1
A Study Report on
HYDROGEN VEHICLE
Fuel Cell Electric Vehicles (FCEV) & Hydrogen Mobility

## Slide 2
1.a Vehicles: Global Hydrogen (FCEV) Outlook – CY 2025
Sales figures in units (Nos.)
World FCEV Sales by Country 2025
Chart: 
| China (7,797) | S. Korea (6,802) | Rest of World (1,412)
Share | 48.7 | 42.5 | 8.8
~16,011
Total FCEV
China
7,797 Nos.
S. Korea
6,802 Nos.
Rest of World
1,412 Nos.
Global FCEV Sales 2020 – 2025 (Nos.)
Chart: 
| 2020 | 2021 ▲83% | 2022 ▲19% | 2023 ▼21% | 2024 ▼22% | 2025 ▲24%
s | 9500 | 17400 | 20704 | 16413 | 12866 | 16011
Top Countries – FCEV Sales 2024 vs 2025
Chart: 
| China | S. Korea | Europe | Japan | USA
2024 | 7113 | 3688 | 736 | 686 | 586
2025 | 7797 | 6802 | 566 | 430 | 365
FCEV vs Battery EV – World Sales 2025
~0.16 L
FCEV sold
~207 L
BEV + PHEV sold
FCEV = <0.1% of electric-vehicle sales; 1 FCEV sold for every ~1,300 plug-in EVs
Hydrogen Refuelling Stations – End 2024
Chart: 
| China | S. Korea | Japan | Germany | USA | France
s | 384 | 198 | 161 | 113 | 89 | 65
World: 1,160 stations
SN | OEM | Key Model | Sales 2025
1 | Hyundai | Nexo (Gen-2) | 7,047 ▲58%
2 | Toyota | Mirai, Crown FCEV | 1,257 ▼
3 | Honda | CR-V e:FCEV | 185
4 | Chinese CV makers | FC buses & trucks | ~7,800 (CN)
➤ China + Korea = 91% of FCEV sales. China's volume is mainly buses & trucks; Korea's is Hyundai Nexo cars. Japan & USA fell ~37%.
Sources: SNE Research via Argus Media & Asia Economy (Feb 2026) – FCEV sales 2020–25; H2stations.org / LBST (Feb 2025) – refuelling stations; IEA Global EV Outlook 2026 – EV sales; IEA Global Hydrogen Review 2025. CN-China
1/25

## Slide 3
1.b Vehicles: India Hydrogen Mobility Outlook – NGHM Pilots
Pilot-stage; no retail FCEV sales
NGHM Transport Pilots – At a Glance
70
H₂ vehicles
12
pilot projects
16
H₂ refuelling stations
₹411 cr
Govt. support
Pilot Vehicles by Phase & Technology
Chart: 
| Phase-1 (Mar'25) | Phase-2 (Jul'26)
Fuel Cell (FCEV) | 15 | 20
H₂-ICE | 22 | 13
37
33
Technology Mix – All 70 Vehicles
Chart: 
| Fuel Cell (35) | H₂-ICE (35)
Mix | 35 | 35
70
Vehicles
Fuel Cell
35 Nos.
H₂-ICE
35 Nos.
SN | Phase-1 Pilot Routes (7 of 10 – all in 1.c)
1 | Greater Noida – Delhi – Agra
2 | Sahibabad – Faridabad – Delhi
3 | Ahmedabad – Vadodara – Surat
4 | Jamnagar – Ahmedabad
5 | Pune – Mumbai
6 | Bhubaneswar – Konark – Puri
7 | Jamshedpur – Kalinga Nagar
Phase-1 Consortium Partners
Vehicle OEMs
Tata Motors
Ashok Leyland
Volvo
Energy & H₂ supply
IOCL
BPCL
HPCL
NTPC
Reliance
ANERT
National Green Hydrogen Mission
₹19,744 cr
Mission outlay till FY 2029-30
5 MMT / yr
Green H₂ production target by 2030
₹208 cr
Phase-1 support (37 vehicles, 9 HRS)
18–24 months
Pilot commissioning timeline
➤ India's H₂ mobility is still at pilot stage, led by buses & heavy trucks. No FCEV car is on retail sale yet (Toyota Mirai pilot with ICAT since 2022).
Sources: PIB / MNRE press release (3 Mar 2025) – Phase-1 pilots; Electrive (10 Aug 2026) & Renewable Watch (31 Jul 2026) – Phase-2 pilots; MNRE – National Green Hydrogen Mission. Other Phase-1 routes: Thiruvananthapuram–Kochi, Kochi–Edappally, Visakhapatnam–Bayyavaram.
2/25

## Slide 4
1.c Vehicles: India H₂ Pilots – Phase-1 Routes (Mar 2025)
37 vehicles · 10 routes
Phase-1 Vehicles by Consortium (Nos.)
Chart: 
| Tata+ IOCL | RIL+ AL | NTPC+ AL | ANERT+ BPCL | HPCL+ Volvo
s | 16 | 10 | 6 | 4 | 1
Phase-1 Technology Mix
Chart: 
| Fuel Cell (15) | H₂-ICE (22)
Mix | 15 | 22
37
Vehicles
Fuel Cell
15 Nos.
H₂-ICE
22 Nos.
Phase-1 At a Glance
5
pilot projects
10
routes
9
H₂ refuelling stations
₹208 cr
Govt. support
SN | Route | State(s) | Consortium | Vehicles | ₹ cr · Refuelling
1 | Greater Noida – Delhi – Agra | Delhi, UP | NTPC + Ashok Leyland | 6 FC buses (12 m) – routes 1 & 6 | 39.05 for both routes
2 | Sahibabad – Faridabad – Delhi | UP, Haryana, Delhi | Tata Motors + IOCL | 2 FC buses + 14 trucks – routes 2–5 | 70.02 · IOCL HRS Faridabad
3 | Ahmedabad – Vadodara – Surat | Gujarat | Tata Motors + IOCL | Shared (H₂-ICE & FC trucks) | IOCL HRS Vadodara
4 | Pune – Mumbai | Maharashtra | Tata Motors + IOCL | Shared | IOCL HRS Pune (being set up)
5 | Jamshedpur – Kalinga Nagar | Jharkhand, Odisha | Tata Motors + IOCL | Shared | Within Tata–IOCL ₹70.02 cr
6 | Bhubaneswar – Konark – Puri | Odisha | NTPC + Ashok Leyland | Shared with route 1 | NTPC H₂ unit at CRUT depot
7 | Thiruvananthapuram – Kochi | Kerala | ANERT + BPCL | 4 trucks (2 FC, 2 H₂-ICE) – routes 7 & 8 | 34.84 · HRS Muttathara 260 kg/d
8 | Kochi – Edappally | Kerala | ANERT + BPCL | Shared with route 7 | HRS Udyogamandal 260 kg/d
9 | Jamnagar – Ahmedabad | Gujarat | Reliance + Ashok Leyland | 2 buses (1 FC, 1 H₂-ICE) + 8 trucks | 46.87
10 | NH-16 Visakhapatnam – Bayyavaram | Andhra Pradesh | HPCL + Volvo | 1 H₂-ICE truck | 17.13
➤ Tata Motors + IOCL hold 4 of 10 routes (16 vehicles); Phase-1 = 10 buses + 27 trucks for ₹207.91 cr – most trucks run on H₂-ICE.
Sources: Lok Sabha unstarred Q1648, MNRE reply (29 Jul 2026) – consortium, routes, vehicles & ₹ sanctioned; PIB/MNRE (3 Mar 2025); The Week (May 2026) – IOCL stations; Indian Infrastructure (Aug 2025) – IOCL Pune; Construction World – Kerala HRS; PTI (24 Dec 2024) – Odisha.
3/25

## Slide 5
1.d Vehicles: India H₂ Pilots – Phase-2 Projects (Jul 2026)
Funding in ₹ crore
Govt. Support by Project (₹ cr)
Chart: 
| ANERT- KSRTC | EKA- KPIT | KPI Green | Waaree | NTPC Green | VECV- BPCL | NHPC
s | 51.5 | 44.8 | 43.4 | 28.8 | 26.6 | 5.9 | 1.8
Phase-2 Vehicles by Type (Nos.)
Chart: 
| FC Bus | FC Truck | H₂-ICE Truck
s | 17 | 3 | 13
Vehicles by State (Nos.)
Chart: 
| Madhya Pradesh | Gujarat* | Kerala | Himachal
s | 16 | 12 | 4 | 1
*incl. Vapi–Nashik (MH) route
SN | Lead / Consortium | Route (State) | Vehicles | ₹ cr
1 | ANERT, KSRTC, Tata Motors | Kochi–Kozhikode; Kochi–Thrissur–Palakkad (KL) | 2 FC bus + 2 H₂-ICE truck | 51.5
2 | EKA Mobility, KPIT, BPCL | Bina–Bhopal / Jhansi / Sanchi (MP) | 8 FC bus + 2 FC truck | 44.8
3 | KPI Green, Tata Motors, AB Process | Vadodara–Ankleshwar; Vapi–Nashik (GJ/MH) | 6 H₂-ICE truck (55 t) | 43.4
4 | Waaree, Indify Horizon | Surat–Chikhli–Tumb (GJ) | 2 FC bus + 1 FC truck | 28.8
5 | NTPC Green Energy | Kandla–Gandhidham (GJ) | 3 FC bus (9 m) | 26.6
6 | VE Commercial Vehicles, BPCL | Bina–Guna (MP) | 1 FC bus + 5 H₂-ICE truck | 5.9
7 | NHPC | Chamba area (HP) | 1 FC bus (9 m) | 1.8
➤ Phase-2: 33 vehicles, ₹202.9 cr (90% of cost). Trucks shift to H₂-ICE (13 of 16) – cheaper than fuel cells; Tata Motors is in 2 of 7 consortia.
Sources: Electrive – India to deploy 33 hydrogen commercial vehicles (10 Aug 2026); Renewable Watch (31 Jul 2026); MNRE / NGHM. Projects to be completed within 24 months of Letter of Award.
4/25

## Slide 6
2. Policy: National Green Hydrogen Mission – Progress
Outlay in ₹ crore
Approved Jan 2023 · ₹19,744 cr to FY 2029-30 · Target ≥ 5 MMT/yr green H₂ by 2030 · ~₹8 lakh cr investment · ~50 MMT/yr CO₂ avoided
Component | Outlay (₹ cr) | Scope | Status (Oct 2026)
SIGHT – electrolyser manufacturing | 17,490 (SIGHT total) | Indian electrolyser factories | 3,000 MW/yr awarded to 15 companies
SIGHT – green H₂ production | within SIGHT | Incentive per kg of green H₂ | 8.62 lakh TPA awarded; ~8,000 TPA running (Feb'26)
Pilot – mobility | 496 | H₂ buses, trucks & stations | 12 projects · 70 vehicles · 16 HRS; ₹41.6 cr released
Pilot – steel | 455 | H₂ in steelmaking | 5 projects; ₹84 cr sanctioned
Pilot – shipping | 115 | Green-fuel bunkering | VOC Port methanol pilot (₹38.1 cr)
Hydrogen hubs | 400 | Port-based H₂ clusters | 3 port hubs; 4 Hydrogen Valley clusters
R&D | 400 | Mission R&D + start-ups | ₹113 cr roadmap; 9 start-ups (₹22 cr)
Total mission | 19,744 | ≥ 5 MMT/yr by 2030 | Skilling: 8,149 trained
₹17,490
SIGHT (89%)
₹1,466
Pilots & hubs
₹400
R&D
₹388
Other
Pilot, hub & R&D outlays (₹ crore)
Chart: 
| Mobility | Steel | Hubs | R&D | Shipping
s | 496 | 455 | 400 | 400 | 115
Hydrogen hubs & valley clusters
Type | Location | Status
Port hub | Deendayal (Kandla), GJ | 1 MW Indian-built plant, Jul 2025
Port hub | V.O. Chidambaranar, TN | Recognised; methanol pilot
Port hub | Paradip, Odisha | Recognised
Valley clusters | Jodhpur, Odisha, Pune, Kerala | 4 HVICs awarded
➤ SIGHT takes 89% of the budget – India funds hydrogen supply first; vehicles get ~2.5% through the ₹496 cr mobility pilot.
Sources: PIB – NGHM progress (28 Oct 2026); Cabinet approval – component outlays (4 Jan 2023); Lok Sabha unstarred Q1648 (29 Jul 2026). Pilot & hub outlays shown to FY 2025-26.
5/25

## Slide 7
Difference Between ICE vs BEV vs FCEV
Parameters | ICE · internal combustion | BEV · battery electric | FCEV · fuel cell electric
Energy source | Petrol or diesel, bought by the litre | Electricity, bought by the kilowatt-hour | Hydrogen gas, bought by the kilogram
Energy stored on board | ≈45 litre tank — about 400 kWh of chemical energy | 40–60 kWh in a lithium-ion pack | 5.6 kg H₂ at 700 bar ≈ 187 kWh (Toyota Mirai)
Energy path | Chemical → heat → mechanical | Chemical → electrical → mechanical | Chemical (H₂) → electrical (fuel cell) → mechanical
Converter | Engine: hundreds of controlled ignitions per second | Motor: one rotating shaft, no combustion | Fuel-cell stack + small buffer battery + motor
Refuel / recharge time | A few minutes | ~35 min for 10–80% on a DC fast charger | 3–5 minutes at 700 bar
Energy reaching the wheels | 12–30% (tank-to-wheel) | Over 77% (grid-to-wheel, including regen) | 40–50% (tank-to-wheel)
Tailpipe | CO₂, NOx and particulates | None | Water vapour only
Waste heat | Large — radiator plus hot exhaust | Small — mainly keeps the pack in range | All heat goes to the coolant; radiator ~2× an ICE's
Status in India | Mass market | Growing — 24.3 lakh EVs sold in FY26 | Pilots only — no FCEV car on sale
In one line: an FCEV refuels like a petrol car and drives like an EV — but turns hydrogen into motion at roughly half a battery car's efficiency.
Sources: ICE & BEV values from the EV study deck; EVreporter (Feb 2026) – FC tank-to-wheel 40–50%; Hyfindr – 3–5 min fill at 700 bar; Toyota UK – Mirai 5.6 kg (×33.3 kWh/kg LHV); FutureBridge – FCEV cooling load; EVreporter – FY26 EV sales.
6/25

## Slide 8
Hydrogen Vehicle Types
Parameters | H₂-ICE | FCEV (car) | Plug-in FCEV | FC hybrid bus / truck
What drives the wheels | An engine burning H₂ (spark ignition) | Electric motor; fuel cell is the main power source | Motor; battery for short trips, fuel cell for long ones | Motor; fuel cell plus a Li-ion pack
Fuel cell | None | Large — 95–128 kW in cars | Main source once battery is low | ~70 kW (Tata–IOCL bus)
Battery | 12 V only | 1.6–2.6 kWh buffer (Nexo) | 17.7 kWh (Honda CR-V e:FCEV) | Li-ion pack, size varies
Electric-only range | None | Minimal | ~47 km (29 miles) | Short — battery assists
Can you plug it in? | No | No | Yes | Depends on design
Tailpipe | Water + some NOx | Water | Water | Water
Efficiency | Diesel-like (engine-limited) | 40–50% tank-to-wheel | ~80%+ on battery miles | Similar to FCEV
Complexity and cost | Lowest: reuses diesel engine lines; no Pt or rare earths | Stack + 700 bar tanks are costly | Stack + bigger battery + charger | Stack + battery + 350 bar roof tanks
Examples | Tata, Reliance–Ashok Leyland, VECV trucks | Toyota Mirai, Hyundai Nexo | Honda CR-V e:FCEV (2024) | Tata–IOCL bus: 30 kg H₂, 300+ km
Where India stands | 35 of 70 NGHM pilot vehicles | No car on sale; Mirai pilot with ICAT | Not available | 26 FC buses + FC trucks in NGHM pilots
Sources: EVreporter (Feb 2026) – H₂-ICE & FC efficiency; Paultan (Apr 2025) – Nexo; Green Car Reports – CR-V e:FCEV; The Week (May 2026) – Tata–IOCL bus; Lok Sabha Q1648 (29 Jul 2026) – NGHM pilot mix (35 FC / 35 H₂-ICE).
7/25

## Slide 9
Basics of Fuel Cell Electrochemistry & Cell Working
H⁺
H⁺
H⁺
Only H⁺
passes
Pt catalyst
splits H₂
Pt catalyst
makes water
H₂ in
Unused H₂
(recirculated)
Air (O₂) in
Water + air
out
M
Electrons (e⁻)
Motor
−
+
Anode (−)
Membrane (PFSA)
Cathode (+)
Anode: H₂ → 2H⁺ + 2e⁻
Cathode: ½O₂ + 2H⁺ + 2e⁻ → H₂O
Overall: H₂ + ½O₂ → H₂O + electricity + heat
Fuel cell vs battery: energy and power are separate
H₂ tank
= ENERGY (kWh)
1 kg H₂ = 33.3 kWh
Stack
= POWER (kW)
Cells in series = VOLTAGE
Motor
Bigger tank = more range; bigger stack = more power. They are sized separately — in a battery, the same cells set both.
One cell gives 1.23 V in theory and ~0.6–0.8 V under load, so hundreds are stacked in series. Mirai Gen-2: 330 cells, 128 kW.
The stack makes power only while H₂ and air flow; a small battery covers start-up, peaks and regenerative braking.
Time to empty = kWh in the tank ÷ kW drawn — just like a battery, but refilled in minutes.
Sources: US DOE – Comparison of Fuel Cell Technologies; Toyota UK – Mirai Gen-2 (330 cells, 128 kW); hydrogen LHV 33.3 kWh/kg; cell voltages are standard PEM electrochemistry values.
8/25

## Slide 10
3.a Fuel Cell: Five generations of the fuel-cell car
GEN 1
1966 – 1990s
Concept & lab cars
GM's Electrovan (1966) was the first fuel-cell road vehicle — a one-off that proved the idea but was far from practical.
HELD BACK BY
Size, weight and cost; stacks were laboratory hardware.
GM Electrovan
GEN 2
2002 – 2012
Lease fleets
Honda FCX and Toyota FCHV (2002) were leased to governments; Honda FCX Clarity (2008) was the first designed for mass production.
HELD BACK BY
Almost no stations; hand-built, very expensive cars.
Honda FCX Clarity · Toyota FCHV
GEN 3
2013 – 2017
First series production
Hyundai ix35 FCEV (2013) and Toyota Mirai (Dec 2014) were built in volume. Mirai Gen-1: 114 kW stack, 4.6 kg H₂.
HELD BACK BY
Thin refuelling networks and high stack cost.
Hyundai ix35 · Toyota Mirai
GEN 4
2018 – 2023
Second generation
Hyundai Nexo (2018): 95 kW, 6.33 kg, 666 km. Mirai Gen-2 (2020): 128 kW, 5.4 kW/L, 5.6 kg, 58% less Pt per kW.
HELD BACK BY
H₂ price and station closures; world sales peaked at 20,704 in 2022.
Hyundai Nexo · Mirai Gen-2
GEN 5
2024 – now
Plug-in & next gen
Honda CR-V e:FCEV (2024) adds a 17.7 kWh plug-in battery. Nexo Gen-2 (2025): 110 kW, 6.69 kg, 700+ km.
HELD BACK BY
Only ~16,000 sold worldwide in 2025; focus is shifting to trucks and buses.
Honda CR-V e:FCEV · Nexo Gen-2
Fuel-cell stack power (kW)
Chart: 
| Mirai Gen-1 (2014) | Nexo Gen-1 (2018) | Mirai Gen-2 (2020) | Nexo Gen-2 (2025)
s | 114 | 95 | 128 | 110
Hydrogen stored on board (kg)
Chart: 
| Mirai Gen-1 | Nexo Gen-1 | Mirai Gen-2 | CR-V e:FCEV | Nexo Gen-2
s | 4.6 | 6.33 | 5.6 | 4.3 | 6.69
➤ Mirai Gen-2 packs 12% more power into a 27% smaller, 41% lighter stack (24 L, 24 kg) with 58% less platinum per kW than Gen-1.
Sources: Wikipedia – Fuel cell vehicle (history); JSME award – Toyota 2nd-gen FC system; Toyota UK – Mirai Gen-2; Paultan (Apr 2025) – Nexo Gen-1/Gen-2; Green Car Reports – CR-V e:FCEV; SNE Research via Asia Economy – world sales.
9/25

## Slide 11
3.b Fuel Cell: Types & mechanism
TYPE | ELECTROLYTE | CARRIER | TEMPERATURE | EFFICIENCY (LHV) | STACK SIZE | WHAT HOLDS IT BACK | IN VEHICLES?
PEMFC Polymer membrane | Perfluorosulfonic acid membrane | H⁺ | < 120 °C | 60% (direct H₂) | < 1 – 100 kW | Expensive Pt catalyst; sensitive to fuel impurities | Yes — every FCEV car, bus & truck
AFC Alkaline | KOH solution or alkaline membrane | OH⁻ | < 100 °C | 60% | 1 – 100 kW | CO₂ in fuel and air poisons the electrolyte | Space & military; niche
PAFC Phosphoric acid | Phosphoric acid in a matrix | H⁺ | 150 – 200 °C | 40% | 5 – 400 kW | Expensive catalyst; long start-up; sulphur sensitive | No — stationary CHP
MCFC Molten carbonate | Molten Li/Na/K carbonates | CO₃²⁻ | 600 – 700 °C | 50% | 300 kW – 3 MW | Hot corrosion; long start-up; low power density | No — utility power
SOFC Solid oxide | Yttria-stabilised zirconia | O²⁻ | 500 – 1,000 °C | 60% | 1 kW – 2 MW | Hot corrosion; long start-up; few shutdowns allowed | Rare — auxiliary power
Why PEM wins in vehicles
Starts fast
Runs below 120 °C, so it reaches power in seconds — high-temperature types take hours to warm up.
Solid membrane
No liquid electrolyte to leak or manage; the solid polymer limits corrosion inside the stack.
Compact & responsive
Follows load changes quickly and packs high power into little space — Mirai Gen-2 reaches 5.4 kW per litre.
➤ PEM is the only fuel cell that starts fast enough and is compact enough for vehicles – the others suit stationary power.
Sources: US DOE Hydrogen & Fuel Cell Technologies Office – Comparison of Fuel Cell Technologies fact sheet; JSME – Toyota 2nd-gen stack (5.4 kW/L).
10/25

## Slide 12
3.c Hydrogen Tank: 350 bar or 700 bar
H₂ at 350 / 700 bar
Boss + in-tank valve + TPRD
Polymer liner
holds the gas (Type IV)
Carbon-fibre wrap
carries the pressure
Outer layer
impact protection
Same fuel. Same fuel cell. Only the storage pressure differs.
That one choice sets how much hydrogen fits, how heavy the tanks are and how complex the station must be — which is why cars use 700 bar and most buses use 350 bar.
 | 350 bar (H35) | 700 bar (H70)
Typical use | City buses and many trucks | Passenger cars
Example | Tata–IOCL bus: 30 kg H₂, 300+ km | Toyota Mirai: 5.6 kg in 3 tanks, ~650 km
Gas density (approx., 15 °C) | ~24 kg/m³ | ~40 kg/m³ — about 1.7× more per litre
Tank type | Type III (metal liner) or Type IV | Type IV (polymer liner + carbon fibre)
Where it fits | Roof or chassis — space is plentiful | Under the floor and seats — space is tight
Fill time | Trucks: 8–20 min (Hyundai XCIENT) | 3–5 min (SAE J2601 protocol)
Station needs | Lower compression | Higher compression + pre-cooling; tank must stay below 85 °C
Safety devices | TPRD, in-tank solenoid valve, check valve | Same
➤ 700 bar stores ~1.7× more hydrogen per litre than 350 bar – vital for cars, less so for buses with a whole roof to use.
Sources: The Week (May 2026) – Tata–IOCL bus; Toyota UK – Mirai Gen-2 tanks; Hyfindr – refuelling line (3–5 min, 85 °C limit); Wikipedia – XCIENT fill time; EVreporter – Type III/IV cylinders; densities are approximate NIST values.
11/25

## Slide 13
Fuel Cell Stack & Hydrogen Tank Layout in the Vehicle
Car (Toyota Mirai Gen-2)
FC
Stack in the front compartment (moved from under the cabin)
3 tanks: one in the centre tunnel, two under the rear seat and boot
84-cell Li-ion battery; 128 kW stack, 134 kW rear motor
5.6 kg H₂ at 700 bar
City bus
FC
Tanks on the roof — plenty of space, and leaks rise away
Fuel cell and battery at the rear
Tata–IOCL: 30 kg H₂ at 350 bar, ~70 kW fuel cell
~1 kg H₂ per 10 km; 300+ km range
Heavy truck
FC
Tanks behind the cab or along the chassis rails
Fuel cell under the cab (FCEV) or H₂ engine in the engine bay (H₂-ICE)
350 or 700 bar
Tata Prima H.55S offered as H₂-ICE and FCEV
Fuel-cell stack
H₂ tanks
Battery
How the parts are packaged
Layout | Benefit | Trade-off
Stack under the floor (Mirai Gen-1) | Keeps weight low | Takes cabin height
Stack in the front bay (Mirai Gen-2, Nexo) | Frees the floor for a third tank | Needs a compact, light stack (24 L, 24 kg)
Tanks under floor and seats (cars) | Protected inside the body structure | Limits storage to ~4–7 kg H₂
Tanks on the roof (buses) | Plenty of volume; leaks rise away from people | Raises the centre of gravity
➤ Hydrogen tanks, not the stack, drive packaging: cars hide 700 bar tanks under the floor; buses put 350 bar tanks on the roof.
Sources: Toyota UK – Mirai Gen-2 layout; JSME – stack size; The Week (May 2026) – Tata–IOCL bus; Autocar Pro – Tata hydrogen truck trials (Prima H.55S); Wikipedia – Nexo/ix35 history.
12/25

## Slide 14
Fuel Cell Control System & Balance of Plant
Fuel-cell stack + supply loops
Air loop
filter → compressor → cathode
H₂ loop
tank → injector → anode → recirculation → purge
Coolant loop
pump → stack → radiator
FCU controller (the brain)
Air: match compressor airflow to the power being asked for
Hydrogen: hold anode pressure, recirculate unused H₂, purge water and nitrogen
Thermal & water: keep the stack near 60–80 °C and the membrane moist — neither flooded nor dry
Boost converter
sets stack current to match demand
Vehicle (via CAN)
power available, H₂ left, warnings
Safety
close tank valves on leak, crash or fault
The control loop: repeats many times every second
1 Measure
Every cell's voltage, H₂ pressure, air flow, coolant temperature, H₂ sensors
2 Estimate
Power available now, membrane wetness, hydrogen left in the tanks
3 Decide
Enough air and H₂? Too hot, too dry or flooded? Any leak?
4 Act
Set compressor and injector, purge, adjust current; shut valves if unsafe
FCU = fuel cell control unit · Balance of plant = compressor, injectors, pumps, valves and sensors around the stack. Toyota's Mirai stacks need no external humidifier.
Sources: JSME award – Toyota 2nd-gen fuel cell system (no humidifier); US DOE – fuel cell fact sheet; FutureBridge – stack operating temperature up to ~80 °C.
13/25

## Slide 15
Hydrogen Refuelling Technology
1 Supply
Tube trailer, pipeline or on-site electrolyser
2 Compressor
Raises pressure in stages
3 Cascade storage
Low, medium and high-pressure banks
4 Pre-cooler
Chills gas before it enters the car
5 Dispenser
350 or 700 bar nozzle
6 Vehicle tank
Must stay below 85 °C
Car ↔ station data link: tank pressure, temperature and volume
Gas heats up as it is squeezed into the tank. Pre-cooling and the SAE J2601 fill protocol keep the carbon-fibre tank below its 85 °C limit while filling in minutes; if the data link drops, the station slows or stops the fill.
Fill pressures in use
Use | Pressure | Typical fill
Cars | 700 bar (H70) | 3–5 minutes
City buses | 350 bar (H35) | 30 kg tanks (Tata–IOCL)
Heavy trucks | 350 or 700 bar | 8–20 minutes (Hyundai XCIENT)
Key standards: SAE J2601 (fill protocol) · ISO 19880-1 (station design) · ISO 19880-5 (hoses) · ISO 14687 (fuel quality)
Hydrogen use – cars (kg per 100 km)
Chart: 
| Mirai Gen-2 | Mirai Gen-1 | Nexo Gen-1
s | 0.84 | 0.94 | 1.02
City bus
~1 kg H₂ per 10 km — a 30 kg tank gives 300+ km (Tata–IOCL bus).
Refuel vs recharge
FCEV car: 3–5 min for a full tank. BEV: ~35 min for 10–80% on a DC fast charger. The FCEV advantage exists only where a 700 bar station is nearby.
➤ A hydrogen car fills in 3–5 minutes – but only where a 700 bar station with pre-cooling exists; buses use simpler 350 bar stations.
Sources: Hyfindr – complete refuelling line (SAE J2601, 85 °C, 3–5 min, ISO 19880-5); Wikipedia – FCEV consumption (from EPA MPGe, ~1 kg ≈ 1 US gal) & XCIENT fill time; The Week (May 2026) – bus figures; EV study deck – BEV charging.
14/25

## Slide 16
PEM Fuel Cell Stack Manufacturing Process Overview
1. Making the membrane electrode assembly (MEA)
1 Catalyst ink
Platinum on carbon mixed with ionomer and solvent
2 Coating
Ink applied to the membrane (decal transfer) or coated directly
3 GDL preparation
Carbon paper or cloth gas diffusion layers cut to size
4 Lamination
Membrane + catalyst + GDL hot-pressed into one MEA
5 Inspection
Check every MEA for leaks, shorts and pinholes
2. Making the stack
Bipolar plates
Metal: stamp thin foil flow fields, then coat against corrosion
Graphite: mould graphite–resin plates
Measure channel depth closely — it sets cell performance
Sealing & stacking
Apply edge seals and gaskets
Stack MEAs and plates in series (330 cells in Mirai Gen-2)
Compress with end plates and tie rods
Conditioning & testing
Break-in run activates the catalyst and wets the membrane (hours to days)
Leak and per-cell voltage tests
Grade and pack
Stacking is often manual; automation must align soft and hard layers without damaging them.
Defects often show up only at stack test — tearing a stack down is costly, so in-line MEA inspection matters.
Thin metal foil can crack during stamping; graphite plates are slow to produce at volume.
➤ Cheaper stacks need continuous coating and lamination, automated stacking and earlier defect detection – not just less platinum.
Source: US DOE Hydrogen & Fuel Cells Multi-Year Program Plan – Manufacturing R&D (PEM stack process steps and challenges); Toyota UK – Mirai Gen-2 cell count.
15/25

## Slide 17
3.d Hydrogen Equipment: Electrolyser Manufacturing Capacity
Global (factory capacity ~58 GW/yr, end-2025)
Share of electrolyser manufacturing capacity (%)
Chart: 
| China | Europe | USA | Others
s | 60 | 20 | 10 | 10
Global snapshot | Figure
Factory capacity, end-2025 | ~58 GW/yr (46 GW/yr a year earlier)
Electrolysers actually made, 2025 | < 5 GW — about 9% utilisation
Installed electrolysis, 2025 | > 4 GW (doubled; China ~¾ of new)
System cost, 2025 | China-made $500–1,100/kW vs others $1,900–2,500/kW
India (SIGHT: 3,000 MW/yr awarded to 15 companies)
India market, 2026 | Figure
Green H₂ production awarded | 8.62 lakh TPA
Green H₂ running (Feb 2026) | ~8,000 TPA
Electrolyser incentive | 3,000 MW/yr in two tranches
SIGHT Tranche I – electrolyser makers (Jan 2024)
Company | MW / yr | Bucket
Reliance Electrolyser Manufacturing | 300 | I
John Cockerill Greenko | 300 | I
Jindal India | 300 | I
Adani New Industries | 198.5 | II
Ohmium Operations | 137 | I
Homihydrogen | 101.5 | II
Advait Infratech | 100 | I
L&T Electrolysers | 63 | I
Total Tranche I | 1,500 | 
➤ India's gap: incentives are awarded, but only ~1% of the awarded green hydrogen (8,000 of 8.62 lakh TPA) is running.
Sources: IEA Global Hydrogen Review 2026 via Argus Media (capacity, utilisation, costs); IEA GHR 2026 executive summary (installed capacity); PIB (28 Oct 2026) – SIGHT progress; Renewable Watch (16 Jan 2024) – SECI Tranche I winners.
16/25

## Slide 18
4. Refuelling Infra: Hydrogen Refuelling Stations
World H₂ stations by country (end-2024)
Chart: 
| China | S. Korea | Japan | Germany | USA | Others
HRS | 384 | 198 | 161 | 113 | 89 | 215
Total
~1,160
China 384
S. Korea 198
Japan 161
Germany 113
USA 89
Others 215
India: EV charging points vs H₂ stations
Chart: 
| EV public charging points | H₂ stations sanctioned (NGHM)
s | 52718 | 16
Who is building India's H₂ stations
IndianOil
NTPC
BPCL
HPCL
Reliance
ANERT
Public-sector firms lead, mostly for pilot fleets. A hydrogen station costs ~5–6× an equivalent CNG station.
Operator | Location | Details | Status
NTPC | Leh, Ladakh (11,562 ft) | 80 kg/day green H₂; 1.7 MW solar; 5 FC buses | Operating — buses handed over mid-2025
IndianOil | R&D Centre, Faridabad (Haryana) | Green H₂ dispensing; Tata FC bus trials | Operating
IndianOil | Gujarat Refinery, Vadodara | Green H₂ dispensing | Operating
IndianOil | Pune, Balasore | Stations for pilot corridors | Being set up
ANERT + BPCL | Muttathara (TVM) & Udyogamandal (Kochi) | 2 stations, 260 kg/day each | Under NGHM pilot
NGHM pilots | 21 routes, 12 projects | 16 stations sanctioned | Phase-1 commissioning by Mar 2027
➤ India's hydrogen network is pilot-scale: 16 sanctioned stations against ~52,700 EV charging points.
Sources: H2stations.org/LBST via Motor1 (Feb 2025); Renewable Watch (20 Jun 2025); The Week (May 2026); Indian Infrastructure (Aug 2025); Construction World – Kerala pilot; Lok Sabha Q1648 (29 Jul 2026); EV study deck – MHI reply (16 Dec 2025); EVreporter (Feb 2026); Electrive (22 Sep 2025).
17/25

## Slide 19
Government Financing & Subsidies for Hydrogen Vehicles
Scheme / instrument | Benefit | Status
NGHM mobility pilots | Viability-gap support of ~90% of project cost; ₹410.77 cr sanctioned for 12 pilots | Active — ₹41.6 cr released
GST on FCEVs | Cut from 12% to 5% under GST 2.0 — same rate as battery EVs | Active (Sep 2025)
MoRTH permit exemption | 7-year permit waiver for hydrogen, electric, ethanol and methanol goods & passenger vehicles (AIS-140 tracker needed) | Notified Jul 2026
SIGHT production incentive | Lowers the cost of green H₂ supply; 8.62 lakh TPA awarded | Active
Private FCEV cars | No central purchase subsidy | None
NGHM mobility funds (₹ crore)
Chart: 
| Earmarked (to FY26) | Sanctioned | Released
s | 496 | 410.8 | 41.6
12% → 5%
GST on FCEVs
7 years
Permit-free operation
How others subsidise fuel-cell vehicles
Country | Support | Result
South Korea | ₩22.5m national + ₩10–12m local subsidy per Nexo — roughly half the ₩69.5m price | Peaked at 10,527 Nexo (2022); 6,802 FCEVs sold in 2025
China | Rewards paid to city clusters (not buyers) for vehicles, fuel-cell supply chain and stations | National goal of 50,000 FCVs by 2025
➤ India funds pilots and tax cuts, not buyers – the opposite of Korea, where subsidies halve the price of a Nexo.
Sources: Lok Sabha Q1648 (29 Jul 2026); PIB (28 Oct 2026); Electrive (22 Sep 2025) – GST; Autocar Pro (8 Jul 2026) – permit exemption; Hydrogen Insight – Korea subsidies; SNE Research via Argus (2025 sales); ICCT – China city clusters.
18/25

## Slide 20
Critical Mineral Mapping for Hydrogen Vehicle Parts
Mineral | Hydrogen part | India supply | Global chokepoint
Platinum | Fuel-cell catalyst (both electrodes) | No commercial mine output — imported | South Africa ~71% of mine supply
Iridium | PEM electrolyser anode | Imported | South Africa ~80% of world supply
Carbon fibre | Type IV H₂ tanks | Not quantified | Few makers worldwide
PFSA ionomer | Fuel-cell & PEM electrolyser membranes | Imported | Few fluoropolymer producers
Nickel | Alkaline electrolyser electrodes | 100% imported | China ~68% of global refining
Rare earths (Nd, Pr, Dy, Tb) | Traction motor magnets | Not quantified | China > 90% of processing
Lithium | Buffer battery | 100% imported | China > 80% of India's Li imports
Where the precious metals go
Fuel cell: platinum on anode and cathode
PEM electrolyser: iridium oxide (anode) + platinum (cathode)
Alkaline electrolyser: nickel-based — no precious metals
One country's share of world supply (%)
Chart: 
| Platinum (S. Africa) | Iridium (S. Africa) | Palladium (Russia) | Rare-earth proc. (China)
s | 71 | 80 | 44 | 90
India's response
Item | Response
Platinum | Thrifting — Mirai Gen-2 uses 58% less Pt per kW
Iridium | Alkaline & AEM electrolysers avoid it; SIGHT backs Indian makers
Engines | H₂-ICE needs no Pt or rare earths — easier to localise
Rare earths | ₹7,280 cr magnet scheme (6,000 t/yr)
Lithium | Reasi (J&K) 5.9 Mt inferred; refinery JV
Sources: USGS Mineral Commodity Summaries 2026 – PGMs (2025e shares); SFA Oxford via Mining Weekly – iridium; IRENA (2020) Table 1 – electrolyser materials; JSME – Mirai Pt; EVreporter (Feb 2026); EV study deck – ORF critical minerals (Jul 2026).
19/25

## Slide 21
Fuel-Cell Powertrain: How Power Flows in an FCEV
H₂ tank
350 / 700 bar
Fuel-cell stack
makes DC power
Boost converter
raises stack voltage
HV DC bus
shares power
Inverter
DC → 3-phase AC
Motor + gear
torque to wheels
Buffer battery
peaks & regen
Regen: motor → inverter → battery
Toyota Mirai Gen-2 example
128 kW stack (330 cells) · 134 kW rear motor
84-cell Li-ion battery: 31.5 kW for 10 seconds
5.6 kg H₂ in 3 tanks · ~650 km range
Three rules
Energy (kWh) = tank size
Power (kW) = stack + battery boost
Battery covers peaks and catches regen
Operating modes
Mode | Fuel cell | Battery | Why
Start-up & creep | Off or warming up | Drives the car | Stack needs air, H₂ and heat first
Steady cruise | Main power source | Topped up with spare power | Fuel cells are most efficient at part load
Hard acceleration | Full power | Adds boost | e.g. Mirai battery adds 31.5 kW for 10 s
Braking | Low or idle | Absorbs regen | A fuel cell cannot store energy
Stopped / idle | Low or off | Runs auxiliaries | Saves hydrogen
Sources: Toyota UK – Mirai Gen-2 powertrain (stack, motor, battery output); US DOE – PEM fuel cell characteristics; battery-hybrid operating logic is the standard FCEV control strategy.
20/25

## Slide 22
Power Electronics: Converting Power in an FCEV
Fuel-cell stack
DC; voltage sags as load rises
FC boost converter
DC → higher, steady DC
HV DC bus
shared by all loads
Inverter
DC → 3-phase AC
Motor
Torque
Buffer battery
via two-way DC-DC
DC-DC converter
HV → 12 V
12 V battery
ECUs, lights, screens
Plug-in FCEV only: AC grid → on-board charger (AC → DC) → battery
Why a boost converter?
A fuel cell's voltage falls as current rises, and depends on how many cells are stacked.
The boost converter lifts and steadies it so the inverter always sees a high, stable bus voltage.
It also controls how much current is drawn from the stack — the FCU uses it to set fuel-cell power.
Toyota calls it the FDC (fuel cell DC-DC converter).
Switch technologies (same as in a BEV)
 | Si IGBT | SiC | GaN
Use | 400 V, low cost | 800 V, premium | Chargers, DC-DC
Efficiency | ~97% | ~98–99% | Very high
Speed | Slower | Fast | Fastest
Cost | Lowest | Higher | Higher
Fast on-off switching (PWM) turns DC into sine-wave AC for the motor.
Sources: Toyota UK – Mirai Gen-2 (fuel cell DC-DC converter); EV study deck – switch technologies; PEM polarisation behaviour per US DOE fuel cell fact sheet.
21/25

## Slide 23
Hydrogen Fuel System: Tank to Stack
Receptacle
H35 / H70 filler
Check valve
stops back-flow
Type IV tanks
700 bar + in-tank valve + TPRD
Regulator
steps pressure down
Injector
meters H₂ to demand
Stack anode
H₂ → 2H⁺ + 2e⁻
Recirculation
pump / ejector returns unused H₂
Purge / drain valve
removes water and nitrogen
Exhaust
water vapour + N₂; H₂ diluted in air
Why step the pressure down?
Tanks store H₂ at up to 700 bar, but the anode needs only a few bar. The regulator drops pressure in stages, and the injector meters exactly the hydrogen the current needs — every 1 kg of H₂ carries about 26.6 kAh of charge (2 electrons per molecule).
Safety devices
TPRD vents the tank safely in a fire
In-tank solenoid valve closes when the car is off or on a fault
H₂ sensors close the tank valves on a leak or crash
Check valve stops gas flowing back out of the filler
Tanks carry leak detection, venting and thermal protection
Fuel-system layouts
Vehicle | Storage
Car | 700 bar; 3 tanks under floor & seats (Mirai)
City bus | 350 bar roof tanks; 30 kg (Tata–IOCL)
Truck | 350 / 700 bar behind the cab
H₂-ICE | Same tanks; injectors at 10–350 bar
➤ Tanks hold 700 bar but the stack sees only a few bar – regulation, recirculation and purging form the hydrogen side of the system.
Sources: EVreporter (Feb 2026) – cylinders, leak detection, injection pressures; Hyfindr – receptacles & refuelling; Toyota UK – Mirai tanks; The Week (May 2026) – bus tanks; charge per kg from Faraday's law.
22/25

## Slide 24
H₂-ICE: How a Hydrogen Combustion Engine Works
H₂ tanks
Type III / IV, 350 or 700 bar
Regulator
drops tank pressure
Injectors
port 10–20 bar or direct up to 350 bar
Spark-ignition engine
lower compression, new pistons
Gearbox & wheels
same driveline as diesel
Exhaust
Water vapour + some NOx → NOx after-treatment may be needed for BS-VI
Diesel → H₂-ICE: what changes
Area | Change
Ignition | Compression ignition → spark plugs, ignition coils
Combustion chamber | Lower compression ratio and redesigned pistons — H₂ burns fast and knocks easily
Fuel system | Hydrogen injectors and pressure regulation replace diesel injection
Materials | H₂-compatible parts to resist embrittlement and leaks
Controls | H₂-calibrated ECU; lean air–fuel ratio (lambda) to cut NOx
Storage | Certified cylinders with leak detection, auto shut-off and venting
H₂-ICE vs FCEV
 | H₂-ICE | FCEV
Efficiency | Diesel-like (engine-limited) | 40–50% tank-to-wheel
Precious metals | None; no rare earths | Platinum catalyst
Localisation | Easier — shares diesel/CNG lines | Longer path; costly stack
Tailpipe | Water + some NOx | Water only
NGHM pilots | 35 vehicles | 35 vehicles
➤ H₂-ICE is the quick, low-cost route for Indian trucks (Reliance–Ashok Leyland, Tata, VECV) – but NOx must still be controlled.
Sources: EVreporter (Feb 2026) – interview with Reliance Industries' head of hydrogen systems (conversion, injection, NOx, cost); Lok Sabha Q1648 (29 Jul 2026) – pilot mix; Autocar Pro – Tata H₂ trucks.
23/25

## Slide 25
High-Voltage, Low-Voltage & Hydrogen Safety Systems
High voltage: orange cables
FC stack + boost
makes and lifts DC power
HV buffer battery
with BMS
PDU
Contactors
Pre-charge
Fuses
Current sensor
Inverter + motor
Air compressor (HV)
Coolant pump & PTC heater
DC-DC converter (HV → 12 V)
Low voltage: 12 V
Powers ECUs, lights, screens, airbags, pumps and steering. The 12 V battery wakes the car.
Hydrogen safety layer
H₂ sensors at the stack, tanks and cabin
Tank valves close on leak, crash or fault
TPRD vents tanks in a fire
Insulation monitor and HVIL, as in a BEV
Power-up: from "start" to "ready" (typical sequence)
1 Wake up
12 V powers the ECUs
2 Check
Insulation, HVIL, H₂ sensors
3 Pre-charge
Battery connects; capacitors fill slowly
4 Open H₂ & air
Tank valves open; compressor starts; stack voltage rises
5 Ready
Fuel cell and battery share the load
Sequence varies by manufacturer; shown for teaching.
Sources: EV study deck – HV/LV architecture and power-up; EVreporter (Feb 2026) – leak detection, auto shut-off, venting; Toyota UK – Mirai Gen-2 components.
24/25

## Slide 26
Thermal & Water Management in an FCEV
Stack coolant loop
Runs up to ~80 °C. Large radiator and fan; low-conductivity coolant because it flows through the live stack.
Battery & e-drive loop
Separate lower-temperature loop for the buffer battery, inverter and motor.
Cabin
Stack waste heat warms the cabin in winter; A/C cools it in summer.
Water management
Water leaves with the exhaust air. The membrane must stay moist; water is purged at shutdown so it cannot freeze — Mirai starts from −30 °C.
Coolant-to-air gap at 40 °C ambient (°C)
Chart: 
| ICE (120 °C coolant) | FCEV (80 °C stack)
s | 80 | 40
Heat to coolant for 20 kW at the wheels (kW)
Chart: 
| ICE | FCEV
s | 20 | 25
Why FCEVs need bigger radiators
An engine dumps about a third of its heat out of the hot exhaust; a fuel cell sends almost all of it to the coolant.
The stack runs cooler, so the gap to outside air is half an engine's — each kW of heat needs more radiator.
Result: roughly 2–2.5× the cooling capacity of an ICE (illustrative estimate).
Operating modes
Situation | What happens
Hot day, high power | Radiator and fan at full; power may be limited to protect the stack
Cold start | Battery drives first while the stack warms itself; water was purged at the last shutdown
Highway cruise | Fuel cell near steady output; radiator carries most of the heat
City traffic | Battery covers peaks and regen; fuel cell runs at part load
Sources: FutureBridge – FCEV thermal challenges (stack ≤80 °C, ΔT and 20 kW example; figures are illustrative); Toyota UK – Mirai −30 °C start; EV study deck – thermal layout.
25/25